## Slide 1
THIẾT KẾ VÀ CÀI ĐẶT MẠNG
Ths. Nguyễn Huỳnh Huy Khoa: CNTT – ĐH Nha Trang
Email: huynh@ntu.edu.vn
SĐT: 077.2567899

## Slide 2: Chapter Two Analyzing Technical Goals and Tradeoffs

## Slide 3: Technical Goals
Scalability
Availability
Performance
Security
Manageability
Usability
Adaptability
Affordability
Notes: Scalability: How much growth a network design must support.
Availability: The amount of time a network is available to users, often expressed as a percent uptime, or as a mean time between failure (MTBF) and mean time to repair (MTTR). Availability goals can also document any monetary cost associated with network downtime.
Security: Goals for protecting the organization's ability to conduct business without interference from intruders inappropriately accessing or damaging equipment, data, or operations. Specific security risks should be documented.
Manageability: Goals for fault, configuration, accounting, performance, and security (FCAPS) management
Usability: Goals regarding the ease with which network users can access the network and its services, including goals for simplifying user tasks related to network addressing, naming, and resource discovery.
Adaptability: The ease with which a network design and implementation can adapt to network faults, changing traffic patterns, additional business or technical requirements, new business practices, and other changes.
Affordability: The importance of containing the costs associated with purchasing and operating network equipment and services.

## Slide 4: Scalability
Scalability refers to the ability to grow
Some technologies are more scalable
  Flat network designs, for example, don’t scale well
Try to learn
  Number of sites to be added
  What will be needed at each of these sites
  How many users will be added
  How many more servers will be added

## Slide 5: Availability
Availability can be expressed as a percent uptime per year, month, week, day, or hour, compared to the total time in that period
  For example:
    24/7 operation
    Network is up for 165 hours in the 168-hour week
    Availability is 98.21%
Different applications may require different levels
Some enterprises may want 99.999% or “Five Nines” availability

## Slide 6: Availability Downtime in Minutes
Notes: 99.70% availability sounds pretty good, but it could mean that the network is down for 0.18 minutes every hour. This is 11 seconds. If those 11 seconds were spread out over the hour, nobody would notice possibly. But if there were some bug, for example, that caused the network to fail for 11 seconds every hour on the hour, people would notice. Users these days are very impatient.
Notice that 99.70% availability also could mean one catastrophic problem caused the network to be down for 1577 minutes all at once. That’s 26 hours. If it were on a Saturday and the network was never down for the rest of the year, that might actually be OK. So, you have to consider time frames with percent availability numbers.
Consider the holy grail: 99.999% availability. That’s 5 minutes downtime per year! Be sure to explain to the customer that scheduled maintenance and upgrades don’t count! Either that or plan for a network with triple redundancy (that could be extremely expensive to implement and operate).

## Slide 7: 99.999% Availability May Require Triple Redundancy
Enterprise
ISP 1
ISP 2
ISP 3
Can the customer afford this?
Notes: In the event of failure of the primary router, the secondary becomes the primary and still has a backup. Fix the previous primary and have it become the tertiary.
This helps with maintenance too. Pull out the tertiary and upgrade it. The primary still has a backup. After extensive testing, put the tertiary back in as the primary. Pull out the original primary and upgrade it. Put it back as the secondary. Finally pull out the original secondary and upgrade it.
Of course, the picture brings up all sorts of other questions because it uses an ISP example.
  Does the customer have provider independent addressing?
  Does the customer have an autonomous system number?
  Are the ISPs really independent? Is there true circuit diversity?
  Are the speeds the same on the three links to the ISPs so that performance degradation is minimized during upgrades or failures?
  Can load balancing be used when all three routers are operational?
  What are the routing protocols inside the enterprise network? Can traffic really get to all three routers, regardless of failures inside the enterprise network? Can the routing protocols adjust to changes?
  Will traffic flow out the “closest” router? Will traffic come in from the Internet via the “closest” entry?
Instructor note: The slide is not meant to be a design recommendation! It’s just a slide to get a discussion going on the ramifications of 99.999% availability.

## Slide 8: Availability
Availability can also be expressed as a mean time between failure (MTBF) and mean time to repair (MTTR)
Availability = MTBF/(MTBF + MTTR)
  For example:
    The network should not fail more than once every 4,000 hours (166 days) and it should be fixed within one hour
    4,000/4,001 = 99.98% availability

## Slide 9: Network Performance
Common performance factors include
  Bandwidth
  Throughput
  Bandwidth utilization
  Offered load
  Accuracy
  Efficiency
  Delay (latency) and delay variation
  Response time

## Slide 10: Bandwidth Vs. Throughput
Bandwidth and throughput are not the same thing
Bandwidth is the data carrying capacity of a circuit
    Usually specified in bits per second
Throughput is the quantity of error free data transmitted per unit of time
    Measured in bps, Bps, or packets per second (pps)

## Slide 11: Bandwidth, Throughput, Load
Offered Load
Throughput
Actual
Ideal
100 % of Capacity
100 % of Capacity

## Slide 12: Other Factors that Affect Throughput
The size of packets
Inter-frame gaps between packets
Packets-per-second ratings of devices that forward packets
Client speed (CPU, memory, and HD access speeds)
Server speed (CPU, memory, and HD access speeds)
Network design
Protocols
Distance
Errors
Time of day, etc., etc., etc.

## Slide 13: Performance (continued)
Efficiency
  How much overhead is required to deliver an amount of data?
  How large can packets be?
    Larger better for efficiency (and goodput)
    But too large means too much data is lost if a packet is damaged
    How many packets can be sent in one bunch without an acknowledgment?

## Slide 14: Delay from the User’s Point of View
Response Time
  A function of the application and the equipment the application is running on, not just the network
  Most users expect to see something on the screen in 100 to 200 milliseconds

## Slide 15: Delay from the Engineer’s Point of View
Propagation delay
  A signal travels in a cable at about 2/3 the speed of light in a vacuum
Transmission delay (also known as serialization delay)
  Time to put digital data onto a transmission line
    For example, it takes about 5 ms to output a 1,024 byte packet on a 1.544 Mbps T1 line
Packet-switching delay
Queuing delay

## Slide 16: Queuing Delay and Bandwidth Utilization
Number of packets in a queue increases exponentially as utilization increases

## Slide 17: Example
A packet switch has 5 users, each offering packets at a rate of 10 packets per second
The average length of the packets is 1,024 bits
The packet switch needs to transmit this data over a 56-Kbps WAN circuit
  Load = 5 x 10 x 1,024 = 51,200 bps
  Utilization = 51,200/56,000 = 91.4%
  Average number of packets in queue =
    (0.914)/(1-0.914) = 10.63 packets

## Slide 18: Delay Variation
The amount of time average delay varies
  Also known as jitter
Voice, video, and audio are intolerant of delay variation
So forget everything we said about maximizing packet sizes
  There are always tradeoffs
  Efficiency for high-volume applications versus low and non-varying delay for multimedia

## Slide 19: Security
Focus on requirements first
Detailed security planning later (Chapter 8)
Identify network assets
  Including their value and the expected cost associated with losing them due to a security problem
Analyze security risks

## Slide 20: Network Assets
Hardware
Software
Applications
Data
Intellectual property
Trade secrets
Company’s reputation

## Slide 21: Security Risks
Hacked network devices
  Data can be intercepted, analyzed, altered, or deleted
  User passwords can be compromised
  Device configurations can be changed
Reconnaissance attacks
Denial-of-service attacks

## Slide 22: Manageability
Fault management
Configuration management
Accounting management
Performance management
Security management

## Slide 23: Usability
Usability: the ease of use with which network users can access the network and services
Networks should make users’ jobs easier
Some design decisions will have a negative affect on usability:
  Strict security, for example

## Slide 24: Adaptability
Avoid incorporating any design elements that would make it hard to implement new technologies in the future
Change can come in the form of new protocols, new business practices, new fiscal goals, new legislation
A flexible design can adapt to changing traffic patterns and Quality of Service (QoS) requirements

## Slide 25: Affordability
A network should carry the maximum amount of traffic possible for a given financial cost
Affordability is especially important in campus network designs
WANs are expected to cost more, but costs can be reduced with the proper use of technology
  Quiet routing protocols, for example

## Slide 26: Network Applications Technical Requirements
Name of Application
Cost of Downtime
Acceptable MTBF
Acceptable MTTR
Throughput Goal
Delay Must be Less Than:
Delay Variation Must be Less Than:

## Slide 27: Making Tradeoffs
Scalability 20
Availability 30
Network performance 15
Security 5
Manageability 5
Usability 5
Adaptability 5
Affordability 15
Total (must add up to 100) 100

## Slide 28: Summary
Continue to use a systematic, top-down approach
Don’t select products until you understand goals for scalability, availability, performance, security, manageability, usability, adaptability, and affordability
Tradeoffs are almost always necessary

## Slide 29: Review Questions
What are some typical technical goals for organizations today?
How do bandwidth and throughput differ?
How can one improve network efficiency?
What tradeoffs may be necessary in order to improve network efficiency?

## Slide 30: Network Traffic Factors
Traffic flow
Location of traffic sources and data stores
Traffic load
Traffic behavior
Quality of Service (QoS) requirements

## Slide 31: Traffic Flow Example
Administration
Business and Social Sciences
Math and Sciences
50 PCs
25 Macs
50 PCs
50 PCs
30 PCs
30 Library Patrons (PCs)
30 Macs and 60 PCs in Computing Center
App 1 108 Kbps
App 2 60 Kbps
App 3 192 Kbps
App 4 48 Kbps
App 7 400 Kbps
Total 808 Kbps
App 1 48 Kbps
App 2 32 Kbps
App 3 96 Kbps
App 4 24 Kbps
App 5 300 Kbps
App 6 200 Kbps
App 8 1200 Kbps
Total 1900 Kbps
App 1 30 Kbps
App 2 20 Kbps
App 3 60 Kbps
App 4 16 Kbps
Total 126 Kbps
App 2 20 Kbps
App 3 96 Kbps
App 4 24 Kbps
App 9 80 Kbps
Total 220 Kbps
Arts and Humanities
Server Farm
10-Mbps Metro Ethernet to Internet

## Slide 32: Types of Traffic Flow
Terminal/host
Client/server
Thin client
Peer-to-peer
Server/server
Distributed computing

## Slide 33: Network Applications Traffic Characteristics

## Slide 34: Traffic Load
To calculate whether capacity is sufficient, you should know:
  The number of stations
  The average time that a station is idle between sending frames
  The time required to transmit a message once medium access is gained
That level of detailed information can be hard to gather, however

## Slide 35: Size of Objects on Networks
Terminal screen: 4 Kbytes
Simple e-mail: 10 Kbytes
Simple web page: 50 Kbytes
High-quality image: 50,000 Kbytes
Database backup: 1,000,000 Kbytes or more

## Slide 36: Traffic Behavior
Broadcasts
  All ones data-link layer destination address
    FF: FF: FF: FF: FF: FF
  Doesn’t necessarily use huge amounts of bandwidth
  But does disturb every CPU in the broadcast domain
Multicasts
  First bit sent is a one
    01:00:0C:CC:CC:CC (Cisco Discovery Protocol)
  Should just disturb NICs that have registered to receive it
  Requires multicast routing protocol on internetworks

## Slide 37: Network Efficiency
Frame size
Protocol interaction
Windowing and flow control
Error-recovery mechanisms

## Slide 38: QoS Requirements
ATM service specifications
  Constant bit rate (CBR)
  Realtime variable bit rate (rt-VBR)
  Non-realtime variable bit rate (nrt-VBR)
  Unspecified bit rate (UBR)
  Available bit rate (ABR)
  Guaranteed frame rate (GFR)

## Slide 39: QoS Requirements per IETF
IETF integrated services working group specifications
  Controlled load service
    Provides client data flow with a QoS closely approximating the QoS that same flow would receive on an unloaded network
  Guaranteed service
    Provides firm (mathematically provable) bounds on end-to-end packet-queuing delays

## Slide 40: QoS Requirements per IETF
IETF differentiated services working group specifications
  RFC 2475
  IP packets can be marked with a differentiated services codepoint (DSCP) to influence queuing and packet-dropping decisions for IP datagrams on an output interface of a router

## Slide 41: Summary
Continue to use a systematic, top-down approach
Don’t select products until you understand network traffic in terms of:
  Flow
  Load
  Behavior
  QoS requirements

## Slide 42: Review Questions
List and describe six different types of traffic flows.
What makes traffic flow in voice over IP networks challenging to characterize and plan for?
Why should you be concerned about broadcast traffic?
How do ATM and IETF specifications for QoS differ?

## Slide 43
Q&A