## Slide 1: Chapter Four Characterizing Network Traffic

## Slide 2: Network Traffic Factors
Traffic flow
Location of traffic sources and data stores
Traffic load
Traffic behavior
Quality of Service (QoS) requirements

## Slide 3: Traffic Flow Example
Administration
Business and Social Sciences
Math and Sciences
50 PCs
25 Macs
50 PCs
50 PCs
30 PCs
30 Library Patrons (PCs)
30 Macs and 60 PCs in Computing Center
App 1 108 Kbps
App 2 60 Kbps
App 3 192 Kbps
App 4 48 Kbps
App 7 400 Kbps
Total 808 Kbps
App 1 48 Kbps
App 2 32 Kbps
App 3 96 Kbps
App 4 24 Kbps
App 5 300 Kbps
App 6 200 Kbps
App 8 1200 Kbps
Total 1900 Kbps
App 1 30 Kbps
App 2 20 Kbps
App 3 60 Kbps
App 4 16 Kbps
Total 126 Kbps
App 2 20 Kbps
App 3 96 Kbps
App 4 24 Kbps
App 9 80 Kbps
Total 220 Kbps
Arts and Humanities
Server Farm
10-Mbps Metro Ethernet to Internet

## Slide 4: Types of Traffic Flow
Terminal/host
Client/server
Thin client
Peer-to-peer
Server/server
Distributed computing

## Slide 5: Network Applications Traffic Characteristics

## Slide 6: Traffic Load
To calculate whether capacity is sufficient, you should know:
  The number of stations
  The average time that a station is idle between sending frames
  The time required to transmit a message once medium access is gained
That level of detailed information can be hard to gather, however

## Slide 7: Size of Objects on Networks
Terminal screen: 4 Kbytes
Simple e-mail: 10 Kbytes
Simple web page: 50 Kbytes
High-quality image: 50,000 Kbytes
Database backup: 1,000,000 Kbytes or more

## Slide 8: Traffic Behavior
Broadcasts
  All ones data-link layer destination address
    FF: FF: FF: FF: FF: FF
  Doesn’t necessarily use huge amounts of bandwidth
  But does disturb every CPU in the broadcast domain
Multicasts
  First bit sent is a one
    01:00:0C:CC:CC:CC (Cisco Discovery Protocol)
  Should just disturb NICs that have registered to receive it
  Requires multicast routing protocol on internetworks

## Slide 9: Network Efficiency
Frame size
Protocol interaction
Windowing and flow control
Error-recovery mechanisms

## Slide 10: QoS Requirements
ATM service specifications
  Constant bit rate (CBR)
  Realtime variable bit rate (rt-VBR)
  Non-realtime variable bit rate (nrt-VBR)
  Unspecified bit rate (UBR)
  Available bit rate (ABR)
  Guaranteed frame rate (GFR)

## Slide 11: QoS Requirements per IETF
IETF integrated services working group specifications
  Controlled load service
    Provides client data flow with a QoS closely approximating the QoS that same flow would receive on an unloaded network
  Guaranteed service
    Provides firm (mathematically provable) bounds on end-to-end packet-queuing delays

## Slide 12: QoS Requirements per IETF
IETF differentiated services working group specifications
  RFC 2475
  IP packets can be marked with a differentiated services codepoint (DSCP) to influence queuing and packet-dropping decisions for IP datagrams on an output interface of a router

## Slide 13: Summary
Continue to use a systematic, top-down approach
Don’t select products until you understand network traffic in terms of:
  Flow
  Load
  Behavior
  QoS requirements

## Slide 14: Review Questions
List and describe six different types of traffic flows.
What makes traffic flow in voice over IP networks challenging to characterize and plan for?
Why should you be concerned about broadcast traffic?
How do ATM and IETF specifications for QoS differ?