## Slide 1: Top-Down Network Design Chapter Five Designing a Network Topology
Copyright 2010 Cisco Press & Priscilla Oppenheimer

## Slide 2: Network Topology Design Themes
Hierarchy - Flat - Mesh
Redundancy
Modularity
Well-defined entries and exits
Protected perimeters

## Slide 3: Why Use a Hierarchical Model?
Reduces workload on network devices
  Avoids devices having to communicate with too many other devices (reduces “CPU adjacencies”)
Constrains broadcast domains
Enhances simplicity and understanding
Facilitates changes
Facilitates scaling to a larger size

## Slide 4: Hierarchical Network Design
Enterprise WAN
Backbone
Campus A
Campus B
Campus C
Building C-1
Building C-2
Campus C Backbone
Core Layer
Distribution Layer
Access Layer

## Slide 5: Hierarchical Network Design

## Slide 6: Hierarchical Design Model
Benefits:
Reduces workload on network devices
Constrains broadcast domains
Enhances simplicity and understanding
Facilitates changes
Facilitates scaling to a larger size

## Slide 7: Hierarchical Design Model
A core layer of high-end routers and switches that are optimized for availability and speed
A distribution layer of routers and switches that implement policies and segment traffic
An access layer that connects users via hubs, switches, and other devices

## Slide 8
  Concentration point at which clients access the network
  Layer 2 switching in the access layer: Defines a single broadcast domain
  Multilayer switching in the campus access layer: Optimally satisfies the needs of a particular user through routing, filtering, authentication, security, or quality of service
  Multilayer switching in the WAN access layer: Helps control WAN costs using dial-on-demand routing (DDR) and static routing
Hierarchical Network – Access Layer
Hierarchical Design Model

## Slide 9
Hierarchical Network – Access Layer
Hierarchical Design Model

## Slide 10
Hierarchical Network – Access Layer
Hierarchical Design Model

## Slide 11
Provides multilayer switching between access and core layers:
Provides media transitions
Aggregates bandwidth by concentrating multiple low-speed access links into a high-speed core link
Determines department or workgroup access
Provides redundant connections for access devices
Hierarchical Network –Distribution Layer
Hierarchical Design Model

## Slide 12
Hierarchical Network –Distribution Layer
Hierarchical Design Model

## Slide 13
Hierarchical Network –Distribution Layer
Hierarchical Design Model
Implements policy-based decisions:
  Filtering by source or destination address
  Filtering on input or output ports
  Hiding internal network numbers by route filtering
  Static routing
  Security
  Quality of service mechanisms

## Slide 14
Hierarchical Design Model
The function of the core layer is to provide fast and efficent data transport that:
Forms a high-speed backbone with fast transport services
Provides redundancy and fault tolerance
Offers good manageabilit
Hierarchical Network – Core Layer

## Slide 15
Hierarchical Design Model
Hierarchical Network – Core Layer

## Slide 16
Flat Loop Topology
Headquarters in Medford
Grants Pass Branch Office
Ashland Branch Office
Klamath Falls Branch Office
FLAT – Mạng phẳng
Mô hình mạng dung cho mạng nhỏ. Không có sự phân cấp, các thiết bị mạng đóng vai trò ngang hàng nhau đảm nhận các công việc giống nhau. Dễ thiết kế triển khai và duy trì theo dõi. Nhưng khó để mở rộng
FLAT

## Slide 17
Flat Versus Hierarchy

## Slide 18
Partial-Mesh Topology
MESH – Mạng lưới
Mạng lưới là topology được kiến nghị để hỗ trợ tính dự phòng, sẵn sàng cho hệ thống bằng việc các thiết bị mạng kết nối với nhau
Mesh

## Slide 19
Mesh
Partial-Mesh Topology
Full-Mesh Topology

## Slide 20
Redundant network designs enable you to meet requirements for network availability by duplicating elements in a network.
Redundancy attempts to eliminate any single point of failure on the network. To enable business survivability after a disaster and offer performance benefits from load sharing, some organizations have completely redundant data centers.
Redundancy – Mạng dự phòng

## Slide 21
Redundancy – Mạng dự phòng
Backup Paths
  How much capacity the backup path supports
  How quickly the network will begin to use the backup path
Load Sharing (Load balancing)

## Slide 22: A Partial-Mesh Hierarchical Design
Headquarters (Core Layer)
Branch Offices (Access Layer)
Regional Offices (Distribution Layer)

## Slide 23
Redundancy – Mạng dự phòng

## Slide 24
Redundancy – Mạng dự phòng

## Slide 25
Redundancy – Mạng dự phòng

## Slide 26
Redundancy – Mạng dự phòng
Before you select redundant design solutions, you should first analyze the business and technical goals of your customer, as discussed in Part I, “Identifying Your Customer’s Needs and Goals.” Make sure you can identify critical applications, systems, internetworking devices, and links. Analyze your customer’s tolerance for risk and the consequences of not implementing redundancy.
Make sure to discuss with your customer the tradeoffs of redundancy versus low cost, and simplicity versus complexity. Redundancy adds complexity to the network topology and to network addressing and routing.

## Slide 27: How Do You Know When You Have a Good Design?
When you already know how to add a new building, floor, WAN link, remote site, e-commerce service, and so on
When new additions cause only local change, to the directly-connected devices
When your network can double or triple in size without major design changes
When troubleshooting is easy because there are no complex protocol interactions to wrap your brain around
Notes: Said by Dr. Peter Welcher, consultant and author of many networking articles in magazines, etc.

## Slide 28: Network Modules
ENTERPRISE EDGE

## Slide 29
Campus
  Cung cấp kết nối đến người dung cuối
  Phân bổ thiết bị đến từng vị trí cơ sở hạ tầng
  Ex: Nhiều tầng của tòa nhà, nhà tòa nhà, nhiều khu vực…
  Cung cấp các dịch vụ ứng dụng đến người dung cuối như data, voice, video..
  Campus nên được thiết kế đảm bảo cung cấp kết nối an toàn đến Data center và truy cập ra ngoài internet
Network Modules

## Slide 30
Data center
  Bao gồm: Servers, Các ứng dụng, Lưu trữ (phục vụ cho người dung bên trong hệ thống mạng và bảo mật đối với bên ngoài.)
  Data center kết nối với Core giúp liên kết trao dỗi dữ liệu với người dung cuối
  Core phải có nhiệm vụ thiết lập các thiết bị định tuyến, thiếc bị truy cập, thiết bị vận chuyển dữ liệu, cân bằng tải…để hỗ trợ người dung kết nối được với khu vực này
Network Modules

## Slide 31
Management
  Cung cấp các theo dõi, phân tích hệ thống, xác thực, các truy cập…
  Quản lý mạng được chia làm hai loại: in-band và out-of-band
  Nên được thiết kế một switch chuyên dụng hoặc Vlan riêng biệt cho quản lý
Network Modules

## Slide 32
Management
  In-band: Sử dụng các giao thức SSH, HTTP, Telnet
  Out-of-band: sử dụng kết nết trực tiếp đến thiết bị quản lý của hệ thống qua cổng console, aux
Network Modules

## Slide 33
WAN Edge
  Là thành phần đảm nhận việc kết nối đến các chi nhanh khác của doanh nghiệp
  WAN Edge thuộc sở hữu của doanh nghiệp hoặc đa phần là từ nhà cung cấp dịch vụ internet
Network Modules

## Slide 34
WAN Edge
Network Modules

## Slide 35
Extranet
  Thành phần này cung cấp các kết nối an toàn đến các đối tác doanh nghiệp, khách hàng, đối tác… truy cập vào hệ thống mạng.
  Ex: Remote-access VPN
Network Modules

## Slide 36
Extranet
Network Modules

## Slide 37
Internet Edge
  Thành phần cung cấp các kết nối cho hệ thống mạng bên trong ra internet.
  Bao gồm DMZ site
Network Modules

## Slide 38
Internet Edge
Network Modules
Enterprise
Enterprise
Enterprise
ISP 1
ISP 1
ISP 2
ISP 1
ISP 1
ISP 2
Enterprise
Option A
Option B
Option C
Option D
Paris
NY
Paris
NY

## Slide 39
Branches
  Cung cấp kết nối đến người dùng ở các site khác của doanh nghiệp sử dụng các dịch vụ.
  Bao gồm: Các LAN kết nối đến site chính thông qua kết nối riêng WAN, Internet thông qua VPN
Network Modules

## Slide 40
Partner site
  Đại diện cho khách hàng, đối tác thông qua Extranet, hay Internet
Network Modules

## Slide 41
E-Commerce
  Bao gồm các host ứng dụng, dịch vụ, dữ liệu sử dụng cho công việc kinh doanh (mua, bán) các sản phẩm
Network Modules

## Slide 42
E-Commerce
  Web and application servers
  Database servers Contain the application and transaction information.
  Firewall and firewall routers: Quản lý kiểm soát truy cập từ bên ngoài
  Network intrusion prevention systems (IPS)
  Multilayer switch with IPS modules
Network Modules

## Slide 43
Teleworker
  Dành cho việc làm việc từ xa (tại nhà, đi công tác) của nhân viên
  Ex: Remote-access VPN, Desktop remote, security Wireless, IP telephony, IP Video.
Network Modules

## Slide 44
Cisco SensorBase
  Đóng vai trò update các mối đe dọa, virus mã đọc, các các, phương thức tấn công…
  Ex: malware, serial attack, email, web security.
Network Modules

## Slide 45
  Campus - Server Farm:
  Chứa các server dịch vụ phục vụ cho hệ thống doanh nghiệp
  Đảm bảo tính toàn vẹn dữ liệu, backup, an toàn bảo mật, hoạt động 24/24…
Network Modules

## Slide 46
  Campus - Server Farm:
Network Modules

## Slide 47
  Campus - Server Farm:
Network Modules

## Slide 48: WLANs and VLANs
A wireless LAN (WLAN) is often implemented as a VLAN
Facilitates roaming
Users remain in the same VLAN and IP subnet as they roam, so there’s no need to change addressing information
Also makes it easier to set up filters (access control lists) to protect the wired network from wireless users

## Slide 49: Summary
Use a systematic, top-down approach
Plan the logical design before the physical design
Topology design should feature hierarchy, redundancy, modularity, and security

## Slide 50: Review Questions
Why are hierarchy and modularity important for network designs?
What are the three layers of Cisco’s hierarchical network design?
What are the major components of Cisco’s enterprise composite network model?
What are the advantages and disadvantages of the various options for multihoming an Internet connection?